## Slide 1: Michael Morris
Deep Reinforcement Learning for UAV Control
Academic Year 2018/19
REFERENCES: T. P. Lillicrap, J. J. Hunt, A. Pritzel, N. Heess, T. Erez, Y. Tassa, D. Silver and D. Wierstra, “Continuous control with deep reinforcement learning,” CoRR, vol. abs/1509.02971, 2016.
Background: Freepik.com
Supervisor: Dr P. Iravani
MEng Integrated Mechanical and Electrical Engineering
Project Outline
VTOL aircraft are capable of fast forward flight and precise low speed manoeuvring. Artificial intelligence provides a novel way of learning an aircraft’s characteristics and controlling it despite their complex flight modes. Reinforcement learning was used as to control the aircraft through its transition between vertical and horizontal flight using modern Artificial Intelligence (AI) techniques.
Simulation
A full flight dynamics model and flight controller model were created. The goal of the AI is to act as the pilot, providing suitable controller inputs.
Exploration
Ornstein-Uhlenbeck noise is added to the actor to force exploration
Through the training process the agent attempts to fly in many different directions while searching for an optimal solution
Reinforcement Learning
An agent interacts with an environment and receives a reward based on its performance. Over time it learns to maximise its reward. Many reinforcement learning algorithms were considered. Deep deterministic policy gradients was chosen as it uniquely works in continuous space
Actor and Critic
Critic
Environment
Actor
State
Reward
Action
Q
Two neural networks control the agent. The ‘critic’ assesses the quality of the agents moves. The ‘actor’ creates actions based on the gradient of the expected quality of its actions.
Forward Planning
When attempting to fly to a goal the agent learns plans ahead and slows down before it gets there. This behaviour is learnt rather than being programmed in
Transition
The agent learnt to accelerate the aircraft my flying downwards before pulling up when the aircraft was past its stall speed
Training Progress
The critic trains first (episode Q0) then when it has a good approximation of the reward function the actor starts to converge.